Design a Computer from Scratch
Appendix B3 – Board Specific Pt 3

---
So far
- Last video
  - Hooked up the 7 segment display
  - Refactored the CPU with separate CPU and CPU_top
  - Made a new Peripheral Memory Map
  - Connected up UART pins
  This video will continue driving the functions we will want to use with the CPU

---
Add Board Specific functions
- Make use of
  - Seven Segment Display
  - USB port
  - VGA
  - I/O Connector(s)
    - Header
    - PMOD connectors

---
Refer to QMTECH Documentation
- Need pin numbers - refer to
  - Code Examples (easiest way)
  - Schematics
- Code Examples
- Used VGA qsf for pin numbers

---
Peripheral Memory Map
- New Peripherals (UART, VGA)
  - Will continue to expand as peripherals get added

---
Added UART and VGA Entities
- I added the UART and VGA from Grant Searles’ Multicomp to CPU_top
- VGA has 5:6:5 R:G:B bits
  - Mapped to the 2:2:2 bits from Grant’s VGA
  - 6850 style contro/status and data interface
  - Used ANSIDisplayVGA.vhd – nicer fonts, more configurable
- UART has 6850 style interface

---
UART/VGA Test Code (Part_B3_Test1.csv)

---
UART/VGA Running
- Code run
  - Type into PuTTY and characters gets echoed to the USB and VDU

---
Add Timer Unit

---
Timer Unit Test Code (Part_B3_Test2.csv)

---
Time Test Results
- Timer works
- LED blinks on for 1 sec, off for 2 secs

---
J12 Connector
- Pins are conveniently marked at the connector on the schematic
- Be careful to not use pin 2

---
J12 on card
- 40 pin connector
- 34 signal pins
- Pin 1 near DC jack on outside edge
- Entity name

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_top_PartB2
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/CPU_top.vhd