Design a Computer from Scratch
Appendix B2 – Board Specific Pt 2

---
So far
Last video drove SDRAM and Ethernet interfaces to inactive levels
This video will begin driving the functions we will want to use with the CPU

---
Add Board Specific functions
- Make use of
  - USB port
  - Seven Segment Display
  - I/O Connector(s)
    - Header
    - PMOD connectors

---
Refer to QMTECH Documentation
- Need pin numbers - refer to
  - Code Examples (easiest way)
  - Schematics
- Code Examples

---
UART
- The UART pins are in the Test05_project_CP2102_UART qsf example file
- Signal names are possibly ambiguous
  - Is uart_rx into the FPGA (ie, transmitted from USB to Serial?)
  - Look at schematic to check
    Pin Y21 is out from the USB to Serial
            and is on uart_rx, so it’s OK (input to
            FPGA)

---
Add UART Loopback
- Add to cpu_001.vhd entity pins
- Let’s test the USB to Serial Interface – add signal
- Add code

---
Test USB-Serial (1/2)
- Run PuTTY
  - Baud rate, etc doesn’t matter
  - Setting to 115,200 baud, No Parity, 8 data bits, 1 stop bit
  - No Hardware handshake
- Device Manager shows COM13 on my PC

---
Test USB-Serial (2/2)
- Type in PuTTY and see it come back
- Not a UART yet but verifies the USB-Serial I/F works
- Could now use Multicomp bufferedUart (skipping for now)

---
Seven Segment Display
The 7 segment display pins are in the Project06_7SEG_LED qsf example file

---
3 Digit Seven Segment Display
- Process described in B1 video
- Code example shows the in/out (in Verilog)
- Convert to VHDL

---
3 Digit Seven Segment Display (2)
- Add to cpu_001.vhd entity
- Created new Peripherals folder
- Created new VHDL file Loadable_7SD_3LED.vhd in new folder

---
3 Digit Seven Segment Display (2)
- Drive Scan_Sig high to turn on digit (one at a time) – inverted by transistor driver
- Drive SMG_Data high to turn on segment – bit order

---
Very Tough Choice
- Could either -
  - Add an entity above the CPU that has the CPU and calls the CPU and peripherals
    - Breaks the top name (will no longer be cpu_001)
    - The CPU is left as a standalone element
  - Or, add a peripheral unit below the CPU
    - All I/O has to be passed through the CPU (top) to get to the device pins
- Tough choice
  - Passing all the pins seems like the worse choice

---
Re-factoring the Design
- Choose to make a new top above the CPU
  - Needed quite a bit of shuffling
- New structure >>>>>>>>>>>>>

---
New CPU entity
- This makes the CPU entity much simpler
- Just has the 50 MHz clock in and the peripheral bus
- Easier to port the CPU to other designs

---
Peripheral Memory Map
- Need a Map for the I/O Peripheral Space
- Will expand as peripherals get added

---
Test Code (Part_B2_Test1.csv)

---
Code Works!
- Press KEY1
  - LED1 lights when pressed
  - 7 Segment Display shows “000” and “001” (Key is inverted sense)
- CPU refactored entity is good
- Added top is good
- Peripherals work
- Code is a lot less messy

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_001_App3
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/cpu_001.vhd