Design a Computer from Scratch
Part A1 – New Opcodes

---
ALU / Branch Control
- Refresher - (from Parts 1-8)
  - Designed a CPU in an FPGA
  - 16 bit instructions
    - 4-bit opcodes (used 7)
    - 4-bit register select (coded 7 or 16)
    - 8-bit data (designed for Multicomp peripherals)
  - 12.5 MIPS (4 of 50 MHz clocks per instruction)
  - 12-bit address code space
  - Peripheral support
    - 8-bits of address, 8-bits of data in/out

---
Objectives
- Add ORI (OR with Immediate value( instruction
- Further test CPU and fix bugs in original design
  - ARI was not writing back after AND (was setting Z-bit)
- Add 4 more registers to Register File (8 R/W registers)

---
Add ORI opcode
- Add ORI (OR with immediate value) opcode
  - Bit-wise OR of selected register and D7..D0 of opcode

---
Add to ALU.vhd
- Add entity
- Add to o_ALU_Out

---
Changes in cpu_001.vhd
- Add to signals
- Add
- Add
- Add

---
Test ORI code
- Code – Part_A1_Test1.csv
- List file shows assembler coding (opcode = 0x9)

---
Missing Write to Register File for ARI/ORI
- Found out that the write back to the register file after ARI (and new ORI) instructions wasn’t happening
- Fixed and now working

---
VHDL code change to fix register file write
- Added code to cpu_001.vhd that fixed register file writes after ARI (and new ORI) opcodes
  - Without these lines, ARI, ORI are more like Bit Test instructions
- Really need a good instruction test program!!!

---
Expand Register File to 8 R/W Registers (1/3)
- In: RegisterFile.vhd
  - Expand signals list

---
Expand Register File to 8 R/W Registers (2/3)
- In: RegisterFile.vhd
  - Add registers (recoded to hex values)

---
Expand Register File to 8 R/W Registers (3/3)
- In: RegisterFile.vhd
  - Add to register output mux (recoded to hex values)

---
Code to Test Register File
LRI each register with a unique value, write to output port

---
Register File Test Result
Works, 8 writes with bouncing bits

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_001_Part9_Condit_Branches
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/cpu_001.vhd