Design a Computer from Scratch
Part 9 – ALU and Conditional Branch Design

---
ALU / Branch Control
- Refresher - Requirements (from Part 2)
  - Used for ARI – AND register immediate
  - Two 8-bits in
    - One input is immediate value on D7..D0
    - Other input is register selected by D11..D8 from Register file
  - One 8-bits out plus Z-bit
  - Opcode determines the ALU operation
    - ARI only instruction so far
    - ORI (OR register immediate) could be added easily
    - ADI (ADD register plus immediate) could be added easily

---
Create VHDL ALU Module
- New File: ALU.vhd
- Entity Name: ALU_Unit

---
ALU Code
Code

---
Signals and Test Pins
Signals / Test pins

---
Add entity to top
- Entity in top
- Comment out

---
ALU Test Code
- File: Part9_Test1.csv
- List file:

---
Test Z-Bit Results
Z bit being set properly

---
Add branch control and test
- Add load PC control for BEZ and BNZ
- Set branch address (absolute)

---
Test Code
Code:
(Part9_Test2.csv)

---
Test Code (lst file)
- Should skip 0x003, 0x007 – Takes both branches
- Tests BNZ, BEZ

---
Results
Skips 0x003, 0x007 (like it should

---
Test Not Taking Branches
- Reverse code
  (Part9_Test3.csv)

---
Test Not Taking Branches
Branches not taken - Working

---
Summary – ALU / Branch Control
- Tested/working
  - Zero Flag working
  - ARI – Working
  - BNZ – Working
  - BEZ – Working
  - Some registers tested, only 4 implemented
- This is all of the design objectives accomplished

---
Resources
- Reduced the ROM size to 512 Words
- CPU only uses 144 logic cells and 2 Memory Blocks

---
Additional Features
- Add subroutine support instructions
  - Branch To Subroutine (BSR) and Return from Subroutine (RTS)
  - Allow code re-use and saves code space
  - Will require a stack to store addresses
- Add ORI instruction
  - Some applications could use it
- Implement all of first 8 registers in register file

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_001_Part9_Condit_Branches
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/cpu_001.vhd