Design a Computer from Scratch
Part 3 – Program Counter Design

---
Program Counter Design
- Refresher - Requirements (from Part 2)
  - 12-bits Program Counter (PC)
  - Loads 0x000 at reset
  - PC controls
    - Increment counter
    - Load counter for branches or jump instruction
    - Branches will use 12-bit absolute addresses
      - Relative branching is not necessary

---
Counter Entity
- File, New
- VHDL File
- Save-As:
  ProgramCounter.vhd
- Make sure folder is the same
  as cpu_001.vhd location
- Select Files to see

---
Copy/Paste to start
- Copy the contents of
  cpu_001 and paste into
  ProgramCounter.vhd
- We will change to add the ports/function we need
- Start with entity pins list
- We will replace the pins with new ones

---
Entity Pins List
- Search/replace cpu_001 to ProgramCounter
- Add Clock, Load, Increment controls
- Add PC Load Value
- Add Output value
- Do we need a reset or will FPGA reset registers automatically?

---
Signals List
- We will use a signal for the PC
- Placed after the ARCHITECTURE and before the BEGIN statements

---
The PC Function
- This needs to be clocked inside a process statement
- Load takes priority over increment

---
Need to add clock to top entity
- Out top only had the KEY0 and LED0
- Add the FPGA clock to the top entity pin list
- This will get connected later to the PC

---
Add the Program Counter to the top
- The counter needs to be instantiated in the top
- Copy the highlighted portion

---
Paste into the top
- Paste into the top
- Goes below the BEGIN in the top
- We will fix/hook it up in the next step

---
Fix Pasted PC Entity
- VHDL has differences between the formatting when an entity is the pin list vs when it is used
- For now change it to leave it dangling
- We will fill in the values before the commas with pins or signals

---
Add Pins
- The only external pin we have is the clock so fill that in
- The rest will be signals

---
Adding signals to top
- Here’s the signals we need to add with default values added
- Here’s the signals used

---
Testing the PC
- There’s guaranteed to be typos and other errors in what we just did
- Maybe you even spotted some of them!
- How can we test this? Ben [Eater] would just insert a 555 and run it slow to look at the address lines with LEDs
- We could use Signal Tap – maybe too advanced at this point?
- Or maybe we could use the pushbutton and LED to do something like what Ben would do!

---
Make a Slow Clock
- If we run the 50 MHz clock into the PC divided by the 2^12 address counts that’s still pretty fast. Too fast to see.
- What about making our own slow clock to test the PC functions? Should be easy enough. We just made a counter after all!
- Let’s put it into the top (cpu_001)
- A clock which generates a single 20 nS pulse around 10 Hz would probably work nicely. 50 Mhz/10Hz is a divide by 5 Million. Let’s pick the nearest power of 2.
  - 2^22 = 4,194,304
  - Looks like a 22 bit counter should fit the bill nicely – will be 12 Hz-ish

---
Making a Slow clock
- 22 bits, one pulse per
- Test this counter on the LED
- The most significant bit should be ~2 Hz
- Need to add the clock pin in the Pin Assignment at Pin_T2

---
“Slow” Blinkey Clock VHDL code
- Worked!
- Signal was
- Code is:
- Sending slower clock out the LED

---
Edge Detect the Slow Clock
- The slow clock needs to be turned into a single clock 20 nS wide pulse every 12 Hz

---
Test the Program Counter Increment
- Clock the w_incPC with the pulse
- Run a PC address bit to the LED
- LED blinks slower
- Pick a higher bit
- LED blinks even slower
- Working

---
Test the Program Counter Load
- Load takes priority over increment
- Set load value
- Use pushbutton to load - invert pushbutton
- Works
- Check specific bit load

---
Move the slow clock to a new VHDL file
Might want this slow clock later

---
Fix top to use new Slow Clock
- Instantiate the slow counter in the top
- Works!

---
Program Counter - Summary
- Built a Program Counter
  - Counter counts
  - Counter loads
- Testing
  - Built a slow clock for testing