Design a Computer from Scratch
Part 4 – ROM Design

---
ROM Design
- Refresher - Requirements (from Part 2)
  - Altera has ROM wizard
  - Need to create initialization contents
  - ROM has registered address inputs
    - Adds a clock delay
      - Control/timing needs to account for this delay
      - Could load one clock before the end of the previous instruction but branches have be finished calculating

---
Create ROM