Design a Computer from Scratch
Part 2 – The CPU Architecture

---
Application Drives Architecture
- Target applications
  - Move around data between 8-bit peripherals
- Peripheral set
  - Borrowed from Multicomp, etc
    - UART (6850 ACIA)
      - USB-Serial on FPGA card
    - VGA monitor
      - VGA on FPGA card
    - PS/2?
      - No PS/2 on FPGA card – could use adapter
  - 256 address I/O space, 8 bit peripheral data

---
FPGA CPU Design Philosophy
  - Wider instruction set than 8-bits is easy in FPGAs
    - Cost is memory cells (we have 56 cells of 1KB)
  - Opcode field width = function of the number of instructions
    - Go for up to 16 instructions = 4 bit opcode field (nibble)
  - 1 or 2 Accumulator(s) involve a lot of shuffling
    - Register file is easy in FPGA
    - Go for up to 16 registers = 4 bit register select (nibble)
  - Immediate loads match peripheral data size
    - 8-bit peripherals

---
Opcode Field Design
  - 16-bit instruction
  - Some typical Instructions
    - Load register with Immediate Value
    - I/O Write from register
    - I/O Read into register
    - AND register with Immediate value
D15..D12	D11..D8	D7..D0
OPCODE	Register Number	Immediate value

---
Flow Control
- Need to be able to loop
  - Jump instruction
- Need to be able to conditionally branch
  - AND register with Immediate value used for checking peripheral status
  - Branch on result Zero
  - Could just have Branch on Zero and do jumps
    - Branch on Not Zero is easy to implement but uses up 1 of the 16 opcodes (implement but keep in back pocket if we need more instructions)

---
Arithmetic Logic Unit
- Need an ALU to perform AND operation
- Need a Zero result flag to use with branch instructions
  - Set when ALU instruction is executed
  - Sticky (until next ALU operation)

---
Program Size / Program Counter
- Branches don’t use D11..D8 register field
- Branches could use full D11..D0
  - Messing around with pages isn’t worth the effort
- Limit program size to 4K words in D11..D0 of opcode
  - Plenty big enough for I/O control programs
D15..D12	D11..D0
OPCODE	Branch address (relative would need adder) / Jump absolute address

---
Opcodes (so far)
Nibble	Opcode	Description
LRI	LRI	Load Register Immediate
ARI	ARI	AND Register Immediate
	IOW	I/O Write
	IOR	I/O Read
	JMP	Jump to an address
	BEZ	Branch if last ALU operation result was zero
	BNZ	Branch if last ALU operation result was not zero

---
Sample Application
LOOP
  IOR Reg0, UART_SR	// Read UART status register
  ARI Reg0, 0x01	// Wait for data present in UART
  BEZ LOOP
  IOR Reg1, UART_DR	// Read UART data into Reg1
  IOW Reg1, VDU_DR	// Write data from Reg1 to VDU
  JMP LOOP	// Repeat forever
- This is actually a useful function! But we will start with a much simpler application – wait for it

---
Pieces We Need to Design
- 12-bit Program Counter
- Register file supporting up to 16 8-bit registers
- ROM for the program
- Peripheral Bus Interface
- Control Timing / Opcode decode
- ALU

---
Program Counter
- 12-bits Program Counter (PC)
- Loads 0x000 at reset
- PC controls
  - Increment counter
  - Load counter for branches or jump instruction
  - Branches will use 12-bit absolute addresses
    - Relative branching is not necessary
- Relatively small Logic Cell usage

---
Register File
- Simplifying assumptions
  - No register to register transfers
  - Same register that was the source of data for ALU operations is also the destination
    - To do otherwise would have required multiple register fields in the instruction
  - Opcode bits D11..D8 select the register to be read or written
  - Multiple clock cycles to read and write ALU result back
    - Implications for Timing C
    - ontrol block
  - Instructions that affect the register file – IOR, IOW, ALU operations

---
Program ROM
- Altera has ROM wizard
- Need to create initialization contents
- ROM has registered address inputs
  - Adds a clock delay
    - Control/timing needs to account for this delay
    - Could load one clock before the end of the previous instruction but branches have be finished calculating

---
Peripheral Bus
- 8 address bits come from D7..D0 of the opcode
- Data only goes out from and in to register file
  - Register number is selected by Opcode D11..D8
- 8-bits separate data in/out connections
  - No need to tristate
- Need write strobe (most peripherals are designed this way)
  - 1 clock wide strobe
- Need read strobe
  - 2 clocks wide strobe

---
ALU
- Used for ARI – AND register immediate
- Two 8-bits in
  - One input is immediate value on D7..D0
  - Other input is register selected by D11..D8 from Register file
- One 8-bits out plus Z-bit
- Opcode determines the ALU operation
  - ARI only instruction so far
  - ORI (OR register immediate) could be added easily
  - ADI (ADD register plus immediate) could be added easily

---
Control Timing / Opcode Decode
- Program Counter control
  - Inc PC, Load PC
- Register File control
  - Load Register File strobe
- ALU set Z-bit

---
Timing / Clock Generation
- FPGA has 50 MHz clock
  - 20 nS
- Need multiple clocks for instruction
  - PC increment
  - ROM address input register > output prop delay
- Use 4 clocks for instruction
  - Code with 2-bit Grey Code for glitch free decodes
    - 00 > 01 > 11 > 10

---
Design Methodology
- Design each element as individual VHDL files
- Combine each element at top level entity
- Then add top above the entity for peripherals
  - Application specific since it uses application peripherals

---
First Application
- Replace Part 1 function
  - Read KEY0
  - Write out to LED0
- Application Memory Map
  - Address = 0x00 , Read, D0 = KEY0
  - Address = 0x00, Write, D0 = LED

---
First Application Code
LOOP
IOR	REG0, 0X00
IOW	REG0, 0X00
JMP	LOOP
- Easy to test – already have the entity from Part 1