Design a Computer from Scratch
Appendix A3 – Assembler Improvements

---
Goals
- Make Assembler independent of external dependencies
  - Currently requires some common Python code from another GitHub
  - Need to fix this so others can run it
- Add some psuedo Instruction
  - Allows expansion of the Instruction set without adding new opcodes

---
Instruction Set
- Currently using 10 opcodes
  - Leaving 6 free opcode values for future expansion of the instructions

---
Add Psuedo NOP
- NOP currently works by using an unimplemented instruction
  - Currently done by the assembler which codes NOP as 0x0
  - This essentially ties up one of the Opcodes leaving only 5 free opcodes
- It would be nice to free the NOP opcode

---
Free the Opcode - Add Psuedo NOP
- Code NOP as an instruction which has no effect, ie, “safe”
  - Example: ORI Reg8, 0x00
  - “Doubly safe” since Reg8 is constant = 0x00 and OR of 0x00 would not change the register even if it could
- Do this in the Assembler
  - Allow source to have NOP
  - Code as: ORI Reg8, 0x00
  - Still show NOP in the listing file

---
Encoding in the assembler
- Current encoding code (Python)
- Replace with

---
List file effects
- List file (before Assembler change)
- List file (after Assembler change)

---
Doing More in the Assembler...
- Created a Psuedo-NOP instruction
  - Interpreted by the Assembler as a “safe” (no effect) instruction
- Some other things can be done by the Assembler
  - Could code other frequently done instructions in the Assembler
- Add “Halt” instruction
  - Allow for multiple HLT instructions so need unique Labels
    - Use address as part of the label

---
Implementing HLT
- HaLT is a jump to self
- Implemented as
  - HALT JMP HALT
- Internally reserve the label H_x
  - X is the address
- Use Psuedo Opcode HLT
- Done in the Assembler

---
Halt as Implemented
- Assembly code
- List file
- Implemented as JMP to self

---
Psuedo Operations
List of Psuedo Opcodes

---
Fix Assembler External Dependencies
- The Assembler has external dependencies
- Resolve external dependencies by adding the imported files into the folder
- Remove sys.path.append(…) from the Assembler

---
Summary
- Resolved external dependencies
  - Now Assembler can be run without hunting down the externals in GitHub
  - Independent code so others can run it
- Added two Psuedo-Ops
  - NOP
  - HLT
  - Set pattern for implementing other Psuedo-Ops in the assembler
- None of these affected the cpu_001 VHDL code

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_001_App3
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/cpu_001.vhd