Design a Computer from Scratch
Part 4 – Register File Design

---
Register File Design
- Refresher - Requirements (from Part 2)
  - Simplifying assumptions
    - No register to register transfers
    - Same register that was the source of data for ALU operations is also the destination
      - To do otherwise would have required multiple register fields in the instruction
    - Opcode bits D11..D8 select the register to be read or written
    - Multiple clock cycles to read and write ALU result back
      - Implications for control block
    - Instructions that affect the register file – IOR, IOW, ALU operations

---
Create Register File Entity
Entity looks like

---
Create single register
- Looks like
- Compiles

---
Add register file to top
- Signals
- Instance in top
- Compiles

---
Input Demultiplexer
- The input has an implicit demultiplexer
- Only the right register is loaded
- Easy to expand

---
Output Multiplexer
- Need an output selector to pick the register
- Easy to expand to more registers

---
Add 3 More Registers to Register File
Signals

---
Add 3 More Registers – Register Loads
Add these into the RegisterFile process

---
Expand Output Multiplexer
Add these lines

---
Add Constants to Register File
- Frequently used values can be stored in the register file
- Used by the IOW or ALU instructions
- Values
  Reg8 = 0x00
  Reg9 = 0x01
  RegF = 0xFF

---
Test Register File
- It would take some serious work to fully test the register file
  - Signal Tap?
- Could test 1 bit of the first register by passing KEY0 through reg0 bit D0 and putting it to LED0

---
Register File Test Code
- In top
- Works – press KEY0, lights LED0
- Routed through the register file

---
Test Read Register Select
- Change w_regSel to select between the reg8 (0x00) and reg9 (0x01)
- View register file D0 on LED0
- Works!
  - Press KEY0, lights LED0

---
Register File - Summary
- Created a register file
  - 4 of 8-bit write/read registers - reg0-reg3
  - Three constants reg8=0x00, reg9=0x01, regF=0xFF
  - Room for 9 more registers or constants
- Minimal Testing
  - Register Select – 3 different registers
  - Load reg0
  - Will test more at a higher level

---
GitHub
- Created a Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU/tree/main
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_001_Part5_RegFile
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/cpu_001.vhd