Design a Computer from Scratch
Part 9 – Shifting (Logical and Arithmetic)

---
So far...
B3 video
  - Created a shift / rotate instruction
    - Had some documentation errors
  - Only did logical shifts
This video will
  - Add Arithmetic Shifts
  - Rename the mnemonics for consistency
  - Add two new Instructions – ADI (Add Immediate to register) and CMP (compare register to immediate value)

---
Add New Instructions
- Add Arithmetic Shifts
  - Rename the mnemonics for consistency
- ADI - Add Immediate to register
- CMP - Compare register to immediate value
  - Add psuedo-mnemonics
    - BEQ Branch if EQual (same opcode bits as BEZ)
    - BNE Branch if Not Equal (same opcode bits as BNX)

---
Shift/Rotate Instruction Changes
- D7 - 0=Left, 1=Right
- D6 – 0=Shift, 1=Rotate
- D5 – 0=Logical, 1=Arithmetic (Shifts only)
- D2-D0 = Shift Count (Only 0x01 currently)

---
Updated Shifter.vhdl Entity
Added Logical/Arithmetic flag

---
Shifter Code

---
Add Logical/Arith Flag to cpu_001.vhd

---
Test Code (Part_9_Test1.csv)
Uses the Land Boards LEDS-SWITCHES Card
- Reads switches to determine which of the Shift/Rotate instructions to run
- Shifts/Rotates a single bit through a register and sends it out to LEDs

---
Use Switches to Control Operation
- Use slide switches on LEDS-SWITCHES card to set the Operation
  - SW1 = Test SRL
  - SW2 = Test SRL
  - SW3 = Test SRL
  - SW4 = Test SRL
  - SW5 = Test SRL
  - SW6 = Test SRL
  - SW7 = Test SRL

---
SRL/RRL Test Code

---
SRL/RRL Test Video

---
Summary
- Added/tested Arithmetic Shift Instructions
- What next???

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_top_PartB2
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/CPU_top.vhd