Design a Computer from Scratch
Part 7 – Peripheral Bus Design

---
Peripheral Bus Design
- Refresher - Requirements (from Part 2)
  - 8 address bits come from D7..D0 of the opcode
  - Data only goes out from and into register file
    - Register number is selected by Opcode D11..D8 (in Register File module)
  - 8-bits separate data in/out connections
    - No need to tristate
  - Need write strobe (most peripherals are designed this way)
    - 1 clock wide strobe
  - Need read strobe
    - 2 clocks wide strobe

---
Peripheral Signals
- 8-bits address
- 8-bits data out
- 8-bits data in
- Write/Read strobes

---
Data Mux to Register File to CPU
- Data mux into register file
  - Data from memory (IOR)
  - Output of ALU (ARI)
  - ROM (LRI immediate instructions)
- Add Opcode decoder signals to select register file input

---
Opcode Decoder
- Signals
- Controls

---
Data Mux to Register File to CPU (pt 2)
- Data mux into register file
  - Data from memory (IOR)
  - Output of ALU (ARI)
  - ROM (LRI immediate instructions)
- ALU faked out for now

---
Peripheral Bus
- Connect up the rest of the Peripheral bus
- Need timing section to generate valid strobe signals

---
Testing Peripheral Code
- Tough to test without having a peripheral
- Could made an I/O peripheral out of KEY0 and LED0
- Strobes need a timing unit
- Could create a program that loops on IOW and see the OP_IOW signal on the LED
  - Would not be too meaningful – 60-50% chance of verifying it is correct
  - No ALU needed for this application

---
Summary
- Created Peripheral bus signals
  - Address, data in/out, controls
- Created Register file input data mux
  - Hooked up immediate values, ALU output (not designed yet), Peripheral read data
- Lack of timing block makes this hard to test
- Didn’t do testing, but it compiles so syntax is likely correct