Design a Computer from Scratch
Part 8 – Opcode Decoder/Timing Design

---
Opcode Decode/Control Timing Design
- Refresher - Requirements (from Part 2)
  - Program Counter control - Inc PC, Load PC
  - Register File control - Load Register File strobe
  - ALU set Z-bit
- Need multiple clocks for instruction
  - PC increment
  - ROM address input register > output prop delay
- Use 4 clocks for instruction
  - Code with 2-bit Grey Code for glitch free decodes
    - 00 > 01 > 11 > 10

---
Clocking Scheme