Design a Computer from Scratch
Part 11 – Instruction Set Changes

---
So far...
Part 10 video ...
  - Added register-to-register transfer function to peripherals
  - Added reset key
  - Added optional nested subroutine LIFO
  - Added Memory Size options

---
In This Video...
- Take a look at the Instruction set
  - Can we free up any Opcode encodes
    - Only have 2 free opcodes
  - Reorder instructions?
- Warning
  - Any code will need to be recompiled if we do any changes and the changes won’t be backwards compatible with previous VHDL code

---
Two unused Opcode Values

---
Free Up an Opcode
How?
- RTS only uses the 4 opcode bits
- S/Rxx has undefined (X) bits
- Constrain S/Rxx

---
Changes to Free One Opcode
- OP B = Reserved
- RTS, OP 3,
  d3 = 1
- S/Rxx OP 3,
  d3 = 0
- Reserve more d4=1 for new opcodes

---
Re-Order Instruction
- Since we’ve already broken the opcode encoding, what else can we break?
  - Hoping to make things better in the end
- ALU operations are scattered all over the place
  - Move them to be adjacent in encoding

---
Before ALU encoding re-ordering
- ALU operations are in three different places
- Move to be adjacent + power of 2 block
- Will reduce decoding logic

---
Put ALU next to each other 0x8-0xb
New encoding will be

---
Put branch/jumps next to each other 0xc-0xf
- JSR, JMP. Bxx encoding will be
- Leave IOR/IOW opcodes at 0x6, 0x7

---
Move LRI/CMP to 0x4, 0x5
- Put LRI/CMP at
- Very similar fields
- Will also reduce decoding

---
Opcodes after Shuffling
- Much cleaner
- Similar things are grouped next to each other

---
Made Opcode Package File
- Single place with [most of the] opcode fields
- File: cpu_001_Pkg.vhd

---
Update Assembler
- Detect in the Assembler if the code is for the old Assembler version
  - Add version number column to header
  - Assembler can see the change and toss up an info box with warning

---
Add I/O Memory Map
- If there’s a file with sourceName_MMAP.csv, then read the file and use as an I/O Memory Map for .lst file
  - Use is optional
  - Tightly constrained header name
- If there is no MMAP.csv file the Assembler
  will still print IO_XX as the address
- See Part9-1_Test1_MMAP.csv for example
- Easier to read code in .lst file

---
Example I/O Memory Map in .lst File

---
Summary
- Refactored the Instruction Set
  - Broke previous code
    - GitHub branches will still do what they did
    - Assembler will match the VHDL if they are both from the same GitHub release or branch
    - Mixing the new Assembler with old VHDL code will not work
    - Running previously compiled code won’t run on the new VHDL
  - Much more “regular” instruction set
  - Created new reserved (for future expansion) instructions
- Added I/O Memory Map capability

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/CPU_top_Part11
  - Also made a v3.0 release
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/CPU_top.vhd