Design a Computer from Scratch
Part 8 – Opcode Decoder/Timing Design

---
Opcode Decode/Control Timing Design
- Refresher - Requirements (from Part 2)
  - Program Counter control - Inc PC, Load PC
  - Register File control - Load Register File strobe
  - ALU set Z-bit
- Need multiple clocks for instruction
  - PC increment
  - ROM address input register > output prop delay
- Use 4 clocks for instruction
  - Code with 2-bit Grey Code for glitch free decodes
    - 00 > 01 > 11 > 10

---
Decoder
Already did most of this in previous Part

---
Timing
- Use 4 clocks for instruction
  - Code with 2-bit Grey Code for glitch free decodes
    - 00 > 01 > 11 > 10
  - Make in Grey Code counter in VHDL module (GreyCode.vhd)
    - Entity

---
Grey Code Counter
- Code
- Includes i_resetN to reset counter at reset

---
Add Grey Code entity to top
- Signals
- Entity in top

---
Wiring up JMP controls
- Flow control
  - JMP – always loadPC
  - Not JMP
- [Remember] Load PC has priority over increment
- Increment / load at state 10 if JMP otherwise just increment at state 10
- Remove default values

---
Wiring up Register File Controls
- w_ldRegF loads at state 10 when doing LRI or IOR instruction
- Remove default value on signal now that we are driving it
- Result

---
Select Register in Register File
Selected register to read/write is the D11..D8 of the instruction

---
Fake out ALU
- No ALU yet
- Fake out ALU
- Change to
- Wrap back ALU output from Register File
- Will create ALU in next part

---
Peripheral Strobes
- 1 clock write at state 11 for IOW
- 2 clocks read at states 11, 10 for IOR
- Usefulness of Grey Code can be seen in the Rd strobe
  - Glitch free

---
Add Peripheral bus to Signal Tap
- Need to first tell Quartus to preserve Peripheral Bus signals
- Use -
- Need to compiler then add in Signal Tap then re-compile

---
Check / Debug Peripheral

---
Block Diagram _ RTL Netlist

---
CPU Performance
- Can now calculate CPU performance
- 50 MHz FPGA clock speed
- 4 clocks per instruction
- 12.5 Million Instructions per Sec (MIPS)
- Good performance for small CPU
- Much faster than TTL computer
  - ROM runs at 50 MHz clk > q

---
Testing
- Lot of untested and under-tested elements
- Use Signal Tap Logic Analyzer tool

---
Configure Signal Tap
- Hardware: USB Blaster
- Select SOF file
  (may be in output folder)

---
Add Signal Tap Clock
- Select … in Signal Configuration
- Node Finder will appear

---
Search for Clock
- Filter: Signal Tap: pre-synthesis
- Click List
- Double Click on i_clock to insert
- Copies to right window
- OK

---
Add Nodes
- Double-click to add nodes
- List to see nodes

---
Add nodes to monitor
- Double click on nodes to add to list
- Click Insert when done then close

---
Set trigger Enable / Conditions
- Click or unclick Trigger Enable
- Set condition (value, edge, level)

---
Monitoring Nodes
Nodes being monitored

---
Compile / Download
- Compile by clicking right arrow
- Download by clicking download button
- Save STP file cpu_002_Part8.stp
- Yes to enable for project

---
Run and capture
Click little blue arrow

---
Debugging
- PC = 0x000, ROM data = 0xE000 (correct)
- Grey code is stuck 0x3

---
Debug / Fix Grey Code Counter
- Fix entity
- Fix load values

---
Re-compile / Run Results
- Grey code now works
- PC works (stays at 0x00)
- Load PC working
- ROM data 0xE000 correct

---
New Test Program
- Unimplemented Opcode (0x0) has no action on registers, I/O or ALU – coded as NOP in Assembler (Part8_Test1.csv)
- Listing file (Part8_Test1.lst)
- Load ROM file (Part8_Test1.MIF)

---
Load New ROM file
- In Heirarchy double click on ROM file
- Select new MIF file
- Compile, download and run

---
Check Output In SignalTap
- Address does count and alternate between 0x000 and 0x001
- ROM data alternates between 0x0000 (NOP) and JMP (0xE000)
- Load PC when address = 0x001 performs JMP to 0x000
- ROM data is one clock after address

---
Check Peripheral Unit
- IOW, IOR strobes, address, data in/out
- New program (Part8_Test2.csv)
- List file

---
Add Peripheral Interface
- There are no Peripherals so Quartus optimizes away the bus
- Create a simple I/O register for test (PeriphTestReg.vhd)
- Write register when address = 0xAA
- Read address when address = 0x55
- Register return compliment of data that was writte

---
Peripheral Test Code
Code

---
Add Peripheral Test Register to top
- Signals
- Code

---
Data Capture IOR, IOW test
- Reads 0x00, writes 0xFF
- Reads 0xFF, writes 0x00
- Peripheral Interface is working

---
Summary – Opcode / Control / Timing
- Tested/working
  - Grey code counter tested
  - PC counter working
  - IOR, IOW with simple peripheral tested
  - LRI Register File Read/Write working
- Still to do
  - No ALU yet
  - No Conditional Branching Flow Control

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU/tree/main
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_001_Part8_ControlUnit
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/cpu_001.vhd