Design a Computer from Scratch
Appendix B1 – Board Specific Pt 1

---
So far
- Created a CPU
- Could be used on any Altera/Intel FPGA card
  - Only uses LED, pushbutton which is on pretty much any FPGA card

---
Taking Care of other Parts
- Tie off unused functions to known voltages
  - Probably OK as-is
  - Better to deliberately make the devices/ports inactive
    - SDRAM
    - VGA
    - Ethernet

---
Add Board Specific functions
- Make use of
  - I/O Connector(s)
    - Header
    - PMOD connectors
  - Seven Segment Display
  - USB port

---
Refer to QMTECH Documentation
- Need pin numbers - refer to
  - Code Examples (easiest way)
  - Schematics
- Code Examples

---
SDRAM
- Pin lists can be found in the .qsf file – save a lot of typing/errors
- Ex: SDRAM qsf file has:

---
Add to cpu_001 entity
- Pattern – Quartus says “Don’t do this” – but I do it
  - Add the signals to the CPU entity with default values
  - Close Project
  - Add pins to cpu_001.qsf file
  - Compile
- Can we create a Board Support package?
  - Could use with all designs using this card

---
First set IO Voltage to 3.3-V LVTTL
- If you don’t do this, Quartus will set the voltage to 2.5V
  - And you will have to fix this in the Pin planner – a lot of clicking….
- Close project (maybe important)
- In cpu_001.qsf, paste (near other similar statements):
- I/O voltages will now default to 3.3V

---
Example: SDRAM Pin DRAM_WE_N
- Add pin to cpu_001.vhd
- Close Project (important?)
- Edit cpu_001.qsf to add
- Save cpu_001.qsf

---
Add DRAM_WE_N
- Open cpu_001 project
- Compile
- View Pin Planner – see that pin was added as assigned
- Make sure to close project when adding pin(s) (follow this sequence otherwise it may not work)

---
Rinse and Repeat
- Can do all SDRAM pins this way – the defaults I used
- Might seem painful but much easier than clicking each pin in Pin Planner and scrolling through list to select the pin

---
Summary
- Tied off unused items on the card to known values
- Added peripheral support

---
GitHub
- Git Hub Repository
  - https://github.com/douggilliland/Design_A_CPU
- Created a branch with progress so far
  - https://github.com/douggilliland/Design_A_CPU/tree/cpu_001_App3
- Top Level entity
  - https://github.com/douggilliland/Design_A_CPU/blob/main/cpu_001.vhd